## Slide 1: How Integers Are Represented in the Computer
Chapter#2

## Slide 2: Unsigned Integer
Most significant bit or msb, is the leftmost bit. In a word msb is bit 15, in a byte, msb is bit 7.
Least significant bit or lsb, is the rightmost bit or bit 0.
Unsigned integer is an integer that represents a magnitude or quantities that can never be negative, such as addresses of memory locations, counters, and ASCII character codes.
All 8 bits in a byte, or 16 bits in a word, are available to represent the number.
largest unsigned integer that can be stored in a byte is 11111111= FFh = 255.
biggest unsigned integer a 16 bit word can hold is 1111111111111111 = FFFFh = 65535.
least significant bit of an integer is 1, then number is odd, and even if the lsb is 0.

## Slide 3: Signed Integer
Signed integer can be positive or negative. The most significant bit is reserved for the sign: 1 means negative and 0 means positive.
Negative integers are stored in the computer in a special way known as two's complement. For example
5 = 0000000000000101
One’s complement of 5 = 11111111111111010
+1
-----------------------------------------------------------
Two’s complement of 5 = 10000000000000000
two's complement of any integer N represent –N.
decimal integer -97 would be represented in 8 bits as 10011111 = 9Fh
in 16 bits. 1111111110011111 = FF9Fh

## Slide 4: Decimal interpretation
Suppose AX contains FE0Ch
unsigned decimal interpretation: Conversion of FE0Ch to decimal yields 65036
Signed interpretation, FE0Ch = 1111111000001100. Since the sign bit is l, this is a negative number, call it -N. To find N, get the two's complement.
N = 0000 0001 11110100=01F4h = 500
Thus, AX contains -500.

## Slide 5: Unsigned & Signed Overflow
For an arithmetic operation such as addition, there are four possible outcomes:
  no overflow
  signed overflow only
  unsigned overflow only
  both signed and unsigned overflows.
Unsigned overflow example on board
MOV AX, FFFFh
MOV BX, 0001h
ADD AX, BX
Signed overflow example on board
MOV AX, 7FFFh
MOV BX, 7FFFh
ADD AX, BX

## Slide 6: The Processor Status & Flag Registers

## Slide 7: Flag Registers
One important feature that distinguishes a computer from other machines is the computer's ability to make decisions.
Circuits in the CPU can perform simple decision making based on the current state of the processor.
For 8086 processor, the processor state is implemented as 9 individual bits called “Flags”
Each decision made by 8086 processor is based on the values of these flags
Flags are placed in FLAG register (16 Bit)
Individual bit positions within register show status of CPU or results of arithmetic operations
Flags are Classified as: Status Flags & Control Flags
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 |  |  |  | OF | DF | IF | TF | SF | ZF |  | AF |  | PF |  | CF

## Slide 8: Flag Registers
Status Flags: reflects results of a computation (affected by machine instructions, used to implement jump instructions, allow programs to have loops/ multiple branches) (located at bit 0, 2,4,6,7 & 11) (Carry, Overflow, Sign, Zero, Auxiliary Carry, Parity)
Control Flags: enable/ disable certain operations of the processor (Located at bit 8,9 & 10) ((Direction, Interrupt, Trap)
Rest of the bits have no significance
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 |  |  |  | OF | DF | IF | TF | SF | ZF |  | AF |  | PF |  | CF

## Slide 9: Flag Registers
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 |  |  |  | OF | DF | IF | TF | SF | ZF |  | AF |  | PF |  | CF

## Slide 10: The Status Flags
Processor uses the status flags to reflect the result of an operation.
For example, If SUB AX,AX is executed, the zero flag becomes 1, thereby indicating that a zero result was produced.
Sub AX, AX
Results in ZF=1
Indicating that a zero result was produced
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 |  |  |  | OF | DF | IF | TF | SF | ZF |  | AF |  | PF |  | CF

## Slide 11: Carry Flag (CF)
Set when the result of an unsigned arithmetic operation is too large to fit into the destination
CF=1; if there is a carry out from the most significant bit (msb) or there is a borrow into the msb on subtraction
CF=0; otherwise
Also affected by the shift & rotate instruction
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 |  |  |  | OF | DF | IF | TF | SF | ZF |  | AF |  | PF |  | CF

## Slide 12: Parity Flag (PF)
Reflects whether the number of 1 bits in the result of an operation is even or odd
PF= 1 ( if the low byte of a result has an even number of one bits; even Parity)
PF= 0 (if the low byte of a result has an Odd number of one bits; Odd Parity)
If a word addition is FFFEh , then low byte contain 7 1’s bits so odd parity
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 |  |  |  | OF | DF | IF | TF | SF | ZF |  | AF |  | PF |  | CF

## Slide 13: Auxiliary Carry Flag (AF)
Set when the result of an operation causes a carry from bit 3 to bit 4
AF= 1, if there is carry out from bit 3 on addition, or a borrow into bit 3 on subtraction
AF=0, otherwise
Significant in binary coded decimal (bcd) operations
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 |  |  |  | OF | DF | IF | TF | SF | ZF |  | AF |  | PF |  | CF

## Slide 14: Zero Flag (ZF)
Set when the result of an arithmetic or logical operation is zero
ZF=1, for a zero result
ZF=0, for a non-zero result
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 |  |  |  | OF | DF | IF | TF | SF | ZF |  | AF |  | PF |  | CF

## Slide 15: Sign Flag (SF)
Set when the result of an arithmetic or logical operation generates a negative result
SF=1, If the msb of a result is 1; representing a negative result in a signed interpretation
SF=0; If the msb of a result is 0; representing a Positive result in a signed interpretation
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 |  |  |  | OF | DF | IF | TF | SF | ZF |  | AF |  | PF |  | CF

## Slide 16: Overflow Flag (OF)
Set when the result of a signed arithmetic operation is too wide to fit into the destination
OF=1, if signed overflow occurred
OF=0, otherwise
processor sets OF= 1 for signed overflow and CF= 1 for unsigned overflow.
For signed interpretation only OF is of interest and CF can be ignored
For an unsigned interpretation CF is important but not OF
On addition of numbers with the same sign, signed overflow occurs when the sum has a different sign.
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 |  |  |  | OF | DF | IF | TF | SF | ZF |  | AF |  | PF |  | CF

## Slide 17: Examples
Instruction Affects flags
MOV/ XCHG. none
ADD/SUB all
INC/DEC all except CF
NEG all
CF = 1 unless result is 0.
OF = 1 if word operand is 8000h or byte operand is 80h

## Slide 18: Examples
ADD AX, BX Where AX =FFFFh & BX = FFFFh
Result stored in AX is FFFEh = 1111 1111 1111 1110.
SF = 1 because the msb is 1 .
PF = 0 because there are 7 (odd number) of 1 bits in the low byte of the result.
ZF = 0 because the result is nonzero.
CF = 1 because there is a carry out of the msb on addition.
OF= 0 because the sign of the stored result is same as that of the number being added.

## Slide 19: Examples
ADD AL, BL Where AL=80h & BL = 80h
Result stored in AL is 00h = 0000 0000.
SF = 0 because the msb is 0.
PF = 1 because all the bits in the result are zero.
ZF = 1 because the result is zero.
CF = 1 because there is a carry out of the msb on addition.
OF= 1 because the sign of the stored result is different as that of the number being added.

## Slide 20: Examples
SUB AX, BX Where AX =8000h & BX = 0001h
Result stored in AX is 7FFFh = 0111 1111 1111 1111.
SF = 0 because the msb is 0 .
PF = 1 because there are 8 (even number) of 1 bits in the low byte of the result.
ZF = 0 because the result is nonzero.
CF = 0 because smaller number is subtracted
OF= 1 In a signed sense, we are subtracting a positive number from a negative one, which is like adding two negatives. Because the result is positive (the wrong sign)

## Slide 21: Examples
INC AL Where AL=FFh
Result stored in AL is 00h = 0000 0000.
SF = 0 because the msb is 0.
PF = 1 because all the bits in the result are zero.
ZF = 1 because the result is zero.
CF = 0 CF is unaffected by INC.
OF= 0 because numbers of unlike sign are being. added

## Slide 22: Examples
NEG AX Where AX =8000h
Result stored in AX is 8000h =1000 0000 0000 0000.
SF = 1 because the msb is 1 .
PF = 1
ZF = 0 because the result is nonzero.
CF = 1 because for NEG CF is always 1 unless the result is 0.

## Slide 23: Exercise
ADD AL,BL where AL=80h and BL=FFh
SUB AX,BX where AX =0000h and BX=8000h
0002h
- FE0Fh
8BCDh
- 71ABh
6389h
+1176h
512Ch
+ 4185h